## Slide 1: UAV Control Systems
Implementation, Protocols, and Vulnerabilities
Kyle Swenson

## Slide 2: Introduction
Military grade systems
  General UAV control overview
    Frequency review
    Frequency bands used and associated characteristics
  Protocols
    CDL, TCDL
  Security
Consumer grade systems
  Communication options
  Range
  Power

## Slide 3: Military UAVs
Two channels:
  Full duplex for control
  Half duplex or simplex for video (downlink)
Operate on multiple frequency bands
  Drone type and size
    Man Portable
    Tactical
    Theater

## Slide 4: Frequency Bands Used by UAVs
UAVs use multiple bands:
  L-Band (800 MHz to 2 GHz)
    Military telemetry
    GPS
  S-Band (2 to 4 GHz)
    Weather radar
    Some satellite communication
    IEEE 802.11
    Unlicensed ISM band in North America (2.4 GHz)
  C-Band (4 to 8 GHz)
    Terrestrial microwave radio relay communication systems
    Open satellite communications: TV networks and raw satellite feeds
    Associated with television receive-only satellite systems
    Weather radar
    Very congested and commonly used

## Slide 5: Frequency Bands Used by UAVs
X-Band (8 to 12 GHz)
  Used by military communications satellites
    Downlink 7.25 to 7.75 GHz, uplink 7.9 to 8.4 GHz
  Not normally used by UAVs
Ku-Band (12 to 18 GHz)
  Designated exclusively for satellite systems
    Some TV broadcast systems depending on location
  Much less interference compared to C-band (fewer civilian uses)
  Doesn’t need to increase power to compensate for noise
  More focused beam than C-Band
    1 meter dish used to differentiate between satellites 2 degrees away
  Vehicle speed detection by law enforcement in Europe
    Non- satellite, used because there is little congestion
  Problems with atmospheric interference
    Rain and snow fade

## Slide 6: RF Communications
General rules:
  As frequency increases, so does
    Cost of equipment
    Weight
    Distance
    Bandwidth
    Power
    Effect of weather impairments
All of these bands except for X-Band have non-military activity
  COTS products exist

## Slide 7: Man Portable Communications
Small drones
  Desert Hawk, Dragon Eye, Pointer, Raven
L-Band digital for control
L-Band analog for video
  1.71-1.85 GHz, 140 MHz Bandwidth
Lower frequencies
  Simpler equipment
  Lower cost
Short range
  About 10 km

## Slide 8: Tactical UAV Communications
Bigger drones
  Hunter, IGNAT, Pioneer, Scan Eagle, Shadow
Use C-Band analog for video downlink (Hunter, IGNAT, Pioneer, Shadow)
  4.4 to 5.85 GHz, 1.45 GHz bandwidth
Scan Eagle
  2.4 GHz for video
Control system depend on UAV model
  C-Band LOS (IGNAT)
  L-Band 900 MHz (Scan Eagle)
  S-Band LOS (Shadow)
    2-4 GHz range
Distance depends on power and equipment
  50 km – 200 km

## Slide 9: Theater UAV Communications
Biggest drones
  Global Hawk, Predator/Warrior A, Reaper
Global Hawk
  Control
    UHF (300 MHz – 3GHz) LOS
      Sub L-Band, L-Band and S-Band
    Ku-Band SATCOM
  Video
    X-Band (7.0 to 11.2 GHz)
    Ku-Band

## Slide 10: Predator and Reaper Communications: LOS
Line of sight data link
  Used for control while in range of GCS
  Used for video downlink for troops on the field
  Video downlink uses C-Band digital
    5.25GHz to 5.85 GHz
http://static.ddmcdn.com/gif/predator-system.gif

## Slide 11: Predator and Reaper Communications: BLOS
Beyond line of sight data link
  Satellite relay
  SATCOM
  Ku-Band
  Used for control, communications relay
http://static.ddmcdn.com/gif/predator-system.gif

## Slide 12: Protocols: CDL
Common Data Link (CDL)
  Full duplex
  Ku Band
    Data rates up to 274 Mbps
  Securable US military communications protocol
    Imagery and signals intelligence
  FY06 Authorization Act
    Requires the use of CDL for all imagery unless a waiver is obtained
    300 pound radios on a small UAV
      Expect a 2 pound version by 2010

## Slide 13: Protocols: CDL
21 May 2013 RFI
  US government asking for ideas to get a CDL radio that can fit on man portable UAVs
    Researchers at Idaho National Laboratories, Idaho Falls
  8 to 10 ounces
  Under 35 W of power
  50 to 110 nautical miles
  Interested in multi-band links
    L, S, C, Ku
  Close link with ground control
    8.448 Mbps to 44.736 Mbps
  Support encryption
  Full TCP/IP capabilities

## Slide 14: Protocols: TCDL
Tactical Common Data Link (development)
  Secure data link designed for UAVs
    Specifically MQ-8B Fire Scout
  In development to transmit:
    Radar, imagery, video and other sensor information
    Rates from 1.544 Mbps to 10.7 Mbps, 200 km range
  Uses Ku band
  Accept data from many different sources
    Encrypt, multiplex, encode, transmit
  Ku narrowband uplink
    Vehicle control
  Ku wideband downlink for data transfer
    Streaming video

## Slide 15: Security
July 2008
  Iraqi Shi’ite militants intercepted live video feeds from Predator
  Unencrypted downlink between UAV and GCS (C-band)
    Video feeds to troops on the ground also use C-Band
  First found drone video on Shi’ite laptop
    Iraq, Afghanistan
    “Its part of their kit now”
  Pentagon has known about the vulnerability since Bosnia campaign in the 1990s
    Assumed that “local adversaries wouldn’t know how to exploit it”
    Claim that encrypting this information is difficult
      The communications protocol is proprietary
      Decade old network is hard to change
      Heavy encryption equipment

## Slide 16: Security
October 2012
  Militants in Iran also captured Predator and Reaper video feeds
  Only 30-40 % of UAVs are using fully encrypted transmissions
  Full encryption expected around 2014
    Problem is that full encryption systems are really heavy
    Motivation behind the RFI, TCDL
    Currently use a mobile-phone size device with AES and triple DES. Slowing integrating these into the fleet
      Much more limited than the RFI desires

## Slide 17: SkyGrabber
Russian software by SkyWare ($26)
  Listens on frequencies and hops around depending on protocol
  Scanning mechanism to determine FHSS sequence of signal
  ‘Decoded’ the UAV FHSS sequence
Developed to intercept music, photos, video, programs.
  Intercepted downloadable content
Possible because the C-Band and Ku-Band also carries internet and TV broadcasts
  Makes the satellites cheap and legal
Lots of tutorials on how to do this

## Slide 18: Consumer Grade Drone Control
Usually uses unlicensed ISM band
  Industrial, scientific and medical
  902 MHz to 928 MHz in Region 1 (North America)
  2.4 GHz to 2.5 GHz
  5.725 GHz to 5.875 GHz

## Slide 19: ISM Band Technology
IEEE 802.11 protocol (WiFi)
  Range varies depending on power and line of sight
  Lots of overhead (software and hardware) for relatively simple control
  Uses a lot of power
  Easy to secure, but easy to hack if not secured
  No custom remote required
    Smartphone, computer, any WiFi device

## Slide 20: ISM Band Technology
Custom ISM
  Requires a custom transceiver and remote
    Increases development time
  Custom protocol
    Makes it difficult to hack even with unencrypted payload
    Minimum overhead
    Custom FHSS sequence
  Less interference with WiFi devices
    Hop to different frequencies (5.8GHz, 2.4 GHz, 900 MHz) if there is too much noise.
  Wide range
    Depending on power, up to 1 km LOS
    Limited by the FCC
  Low power
    Sacrifice range to increase battery life

## Slide 21: Questions?

## Slide 22: Sources
http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=1460867&tag=1
http://www.bth.se/fou/cuppsats.nsf/all/e91df00b763f080cc12572990052d819/$file/Masters_Thesis%5B1%5D.pdf
http://science.howstuffworks.com/predator6.htm
http://defense-update.com/products/p/predator.htm
http://info.publicintelligence.net/JSC-04-054.pdf
http://cryptome.org/predator-read.pdf
http://online.wsj.com/news/articles/SB126102247889095011
http://www.advtecheng.com/uploads/ATEI_Ku-Band_Opt_Trade.pdf
http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=4106321&tag=1
https://www.google.com/url?sa=t&rct=j&q=&esrc=s&source=web&cd=16&ved=0CEYQFjAFOAo&url=http%3A%2F%2Fwww.dtic.mil%2Fcgi-bin%2FGetTRDoc%3FAD%3DADP010757&ei=PkVpUrDjI4jTigKNsoDwBQ&usg=AFQjCNHWoDGA-oEKbWo5m6u9OniiXPfwfg&cad=rja
http://www.nps.edu/Academics/Institutes/Meyer/docs/A%20study%20of%20reconnaissance%20surveillance%20UAV.pdf
http://www.telesat.com/sites/default/files/telesat/files/whitepapers/UAV-Briefing.pdf
http://ftp.rta.nato.int/public/PubFulltext/RTO/MP/RTO-MP-044/MP-044-B10.pdf
http://web.ecs.baylor.edu/faculty/dong/paper/dong_wcnc07_T2S05P05.pdf
http://www.richardsilverstein.com/2013/10/09/third-israeli-drone-sabotaged-by-hacking/
http://www.homelandsecuritynewswire.com/pentagon-says-us-fixed-drones-hacked-iraqi-insurgents
http://www.google.com/hostednews/afp/article/ALeqM5gVfpsQcogZoD0Bx0efyryW0QK63Q?hl=en
http://www.dailytech.com/Iran+Yes+We+Hacked+the+USs+Drone+and+Heres+How+We+Did+It/article23533.htm
http://resources.infosecinstitute.com/hacking-drones-overview-of-the-main-threats/
http://www.syssec.ethz.ch/research/ccs139-tippenhauer.pdf
http://jiangbian.info/papers/2013/uav-wsn-icns-2013-abstract.pdf
http://www.electronicsweekly.com/news/design/communications/avionics-security-challenges-in-unmanned-vehicle-development-2009-07/
http://en.wikipedia.org/wiki/C_band
http://privat.bahnhof.se/wb907234/killuav.htm
http://12160.info/profiles/blogs/how-to-kill-a-drone-since-drones-can-kill-americans-americans-can
http://gizmodo.com/5906292/flying-your-own-military-drone-a-user-manual
http://info.publicintelligence.net/JFCOM-UAS-PocketGuide.pdf
http://privat.bahnhof.se/wb907234/pics/skygrab.pdf
http://info.publicintelligence.net/JSC-03-024.pdf
http://publicintelligence.net/dod-joint-spectrum-center-predator-drone-frequency-analysis-reports/
http://www.wired.com/dangerroom/2012/10/hack-proof-drone/
http://en.wikipedia.org/wiki/Common_Data_Link
http://jitc.fhu.disa.mil/brochure/cdl_.pdf
http://www.fas.org/irp/program/disseminate/tcdl.htm
http://uscrow.org/2013/08/05/how-to-kill-predator-drones-uavs/
http://www.gdfortress.com/Technology-Article/44-ghz-c-band.html
http://www.level421.com/index.php?id=1721
http://www.scatmag.com/technical/techarticle-mar05.pdf
http://en.wikipedia.org/wiki/K_band
http://www.militaryaerospace.com/articles/2013/05/Small-UAV-CDL.html
https://www.fbo.gov/index?s=opportunity&mode=form&id=5fa993abd4c637827fd0bda5718ed3ce&tab=core&_cview=1
http://www.inetdaemon.com/tutorials/satellite/communications/frequency-bands/